## Slide 1: UNDERWATER IMAGE ENHANCEMENT USING COLOR BALANCE AND FUSION
GUIDED BY
Mr. ELANGO.B,
Asst. PROFESSOR,
DEPT. OF E.C.E.
DONE BY
VISHNU PRASATH.S 420419106029
PUGAZHENTHI.K 420419106021
SANTHOSH.S 420419106023
FIRST REVIEW ON

## Slide 2: INTRODUCTION
Reconstruction of underwater object from sequence of images distorted by moving water waves is challenging task. Underwater image processing is necessary due to quality of image captured.
This image suffers from quality degradation, distortion, blurring. When taking a picture of an underwater object from outside the water container, waves on the surface cause distortion. If series of pictures are taken at various times, different distortions will be seen in each picture.

## Slide 3: COND..,
The image seen by the camera is distorted by refraction as a function of both the angle of the water surface normal at the point of refraction and the amplitude of the water waves.
If the water is perfectly flat (i.e., there are no waves), there will be no distortion due to refraction However, if the surface of the water is being disturbed by waves, the nature of the image distortion becomes considerably more complex.

## Slide 4: COND..,
Underwater imaging is widely used in ocean exploration and other fields; however, due to absorption and scattering effects from the environment, serious degradation exists in underwater images, mainly in the form of noise, blur, etc.
Reconstruction of underwater image is challenging task. Underwater images may contain distortions. Distortion may be due to both motion blur and refraction. It also contains some quality degradation, so that it is necessary to improve the quality of images. Reconstruction of images from blurred and noisy images may improve the quality of images.
To recover the object from such distorted images is challenging task.

## Slide 5: ABSTRACT
Underwater images when captured for different applications and analysis, they are degraded in quality and visual parameter; also there is sometimes information loss. Here the paper presents the methodology to improve the quality of underwater images which has been degraded due different distortions like noise, light, motion blur, scattering, waves of water, color change etc. The first approach is to implement white balance for reducing color cast efficiently and Enhancing the underwater images called mixture Contrast Limited Adaptive Histogram Equalization (CLAHE) color model.

## Slide 6: COND..,
The method operates Contrast Limited Adaptive Histogram Equalization on RGB and HSV color model and Euclidean norm is used to combine both results together. The combined results show less mean square error and high peak signal to noise ratio(PSNR) then other methods of under water image enhancing. It shows that the projected method is capable of classifying coral reefs particularly when visual cues are visible .Finaly the weights which are one of the ways where we restore specific required information in image for better image fusion results. After fused to overall enhance the underwater image quality thus making it more informative.

## Slide 7: OBJECTIVES
The main objective of the project is to recover the object from distorted images using image processing techniques.

## Slide 8: SCOPE OF THE PROJECT
We have proposed an alternative approach to enhance underwater images. Our strategy builds on the fusion principle and does not require additional information than the single original image.
the main scope is that our approach able to enhance a wide range of underwater images (e.g. different cameras, depths, light conditions)with high accuracy,being able to recoverimportant faded features and edges.
Moreover, the utility and relevance of the proposed image enhancement technique for several challenging underwater computer vision applications.

## Slide 9: EXISTING SYSTEM
There have been several attempts to restore and enhance the visibility of such degraded images. Since the deterioration of underwater scenes results from the combination of multiplicative anda dditive processes traditional enhancing techniques such as gamma correction, histogram equalization appear to be strongly limited for such a task.

## Slide 10: DISADVANTAGES
Existing system having number of issues that reduce their practical applicability.
cannot reduce color cost efficiently.

## Slide 11: PROPOSED SYSTEM
In proposed system we use 3 approach. firstly, to implement white balance for reducing color cast efficiently and Enhancing the underwater images called mixture Contrast Limited Adaptive Histogram Equalization (CLAHE) color model.
The method operates Contrast Limited Adaptive Histogram Equalization on RGB and HSV color model and Euclidean norm is used to combine both results together.

## Slide 12: COND..,
The combined results show less mean square error and high peak signal to noise ratio(PSNR) then other methods of under water image enhancing. It shows that the projected method is capable of classifying coral reefs particularly when visual cues are visible .
Finally the weights which are one of the ways where we restore specific required information in image for better image fusion results. After fused to overall enhance the underwater image quality thus making it more informative.

## Slide 13: BLOCK DIAGRAM
underwater Input image
CLAHE
image fusion
white balance
output image