## Slide 1: UNDERWATER IMAGE ENHANCEMENT USING COLOR BALANCE AND FUSION
SECOND REVIEW ON
GUIDED BY
Mr. ELANGO.B,
Asst. PROFESSOR,
DEPT. OF E.C.E.
DONE BY
VISHNU PRASATH.S 420419106029
PUGAZHENTHI.K 420419106021
SANTHOSH.S 420419106023

## Slide 2: INTRODUCTION
Reconstruction of underwater object from sequence of images distorted by moving water waves is challenging task. Underwater image processing is necessary due to quality of image captured.
This image suffers from quality degradation, distortion, blurring. When taking a picture of an underwater object from outside the water container, waves on the surface cause distortion. If series of pictures are taken at various times, different distortions will be seen in each picture.

## Slide 3: COND..,
The image seen by the camera is distorted by refraction as a function of both the angle of the water surface normal at the point of refraction and the amplitude of the water waves.
If the water is perfectly flat (i.e., there are no waves), there will be no distortion due to refraction However, if the surface of the water is being disturbed by waves, the nature of the image distortion becomes considerably more complex.

## Slide 4: COND..,
Underwater imaging is widely used in ocean exploration and other fields; however, due to absorption and scattering effects from the environment, serious degradation exists in underwater images, mainly in the form of noise, blur, etc.
Reconstruction of underwater image is challenging task. Underwater images may contain distortions. Distortion may be due to both motion blur and refraction. It also contains some quality degradation, so that it is necessary to improve the quality of images. Reconstruction of images from blurred and noisy images may improve the quality of images.
To recover the object from such distorted images is challenging task.

## Slide 5: ABSTRACT
Underwater images when captured for different applications and analysis, they are degraded in quality and visual parameter; also there is sometimes information loss. Here the paper presents the methodology to improve the quality of underwater images which has been degraded due different distortions like noise, light, motion blur, scattering, waves of water, color change etc. The first approach is to implement white balance for reducing color cast efficiently and Enhancing the underwater images called mixture Contrast Limited Adaptive Histogram Equalization (CLAHE) color model.

## Slide 6: COND..,
The method operates Contrast Limited Adaptive Histogram Equalization on RGB and HSV color model and Euclidean norm is used to combine both results together. The combined results show less mean square error and high peak signal to noise ratio(PSNR) then other methods of under water image enhancing. It shows that the projected method is capable of classifying coral reefs particularly when visual cues are visible .Finaly the weights which are one of the ways where we restore specific required information in image for better image fusion results. After fused to overall enhance the underwater image quality thus making it more informative.

## Slide 7: OBJECTIVES
The main objective of the project is to recover the object from distorted images using image processing techniques.

## Slide 8: SCOPE OF THE PROJECT
We have proposed an alternative approach to enhance underwater images. Our strategy builds on the fusion principle and does not require additional information than the single original image.
the main scope is that our approach able to enhance a wide range of underwater images (e.g. different cameras, depths, light conditions)with high accuracy,being able to recoverimportant faded features and edges.
Moreover, the utility and relevance of the proposed image enhancement technique for several challenging underwater computer vision applications.

## Slide 9: LITERATURE SURVEY 1
S.NO | TITLE | AUTHOR | YEAR | CONTENTS
1 | Underwater image processing: state of the art of restoration and image enhancement methods | Michele Ruta; Floriano Scioscia; Giuseppe Loseto; Eugenio Di Sciascio | July 2020. | presented restoration of underwater Images by fusion method. In the paper they presented novel strategy which enhances the visibility of underwater images effectively. They have focused on image fusion which is contributed by different weight map images. The algorithm consists of different inputs mainly computed from minmax enhanced and white balanced of input distorted image

## Slide 10: LITERATURE SURVEY 2
S.NO | TITLE | AUTHOR | YEAR | CONTENTS
2. | Underwater image processing: state of the art of restoration and image enhancement methods | Liming Chen; Chris Nugent; George Okeyo | Feb. 2019 | presented novel strategy to enhance underwater images and videos by fusion. Their approach was first to decrease the temporal coherent noise from the image. They have also defined different weight map for videos as Laplacian contrast weight, Local contrast Weight, Saliency weight, exposedness weight. Then fused image is obtained by fusion of input image with the weights

## Slide 11: LITERATURE SURVEY 3
S.NO | TITLE | AUTHOR | YEAR | CONTENTS
3. | Control of underwater vehicles in full unsteady ﬂow | Jin Wang; Jiayi Cao; Bin Li; Sungyoung Lee; R. Simon Sherratt | November 2015 | Multisensor image fusion technique for reconstruction of images, wavelet based image fusion technique was used to get improvement in resolution of images.

## Slide 12: LITERATURE SURVEY 4
S.NO | TITLE | AUTHOR | YEAR | CONTENTS
4. | Enhancing underwater images and videos by fusion | Luigi Atzori; Antonio Iera; GiacomoMorabito | January 2021 | It has compared different image fusion techniques with PSNR peak signal to noise ratio, EN entropy, and MSE mean squared error. Thus image fusion using wavelet transform gives better results as compared to other methods. Review results that spatial domain provide high spatial resolution, But spatial domain has image blurring problem. Wavelet transform is a very good technique for image fusion which provides high quality spectral content.

## Slide 13: EXISTING SYSTEM
There have been several attempts to restore and enhance the visibility of such degraded images. Since the deterioration of underwater scenes results from the combination of multiplicative anda dditive processes traditional enhancing techniques such as gamma correction, histogram equalization appear to be strongly limited for such a task.

## Slide 14: DISADVANTAGES
Existing system having number of issues that reduce their practical applicability.
cannot reduce color cost efficiently.

## Slide 15: PROPOSED SYSTEM
In proposed system we use 3 approach. firstly, to implement white balance for reducing color cast efficiently and Enhancing the underwater images called mixture Contrast Limited Adaptive Histogram Equalization (CLAHE) color model.
The method operates Contrast Limited Adaptive Histogram Equalization on RGB and HSV color model and Euclidean norm is used to combine both results together.

## Slide 16: COND..,
The combined results show less mean square error and high peak signal to noise ratio(PSNR) then other methods of under water image enhancing. It shows that the projected method is capable of classifying coral reefs particularly when visual cues are visible .
Finally the weights which are one of the ways where we restore specific required information in image for better image fusion results. After fused to overall enhance the underwater image quality thus making it more informative.

## Slide 17: BLOCK DIAGRAM
underwater Input image
CLAHE
image fusion
white balance
output image

## Slide 18: WHITE BALANCE
White balance (WB) is the process of removing unrealistic color casts, so that objects which appear white in person are rendered white in your photo. Proper camera white balance has to take into account the "color temperature" of a light source, which refers to the relative warmth or coolness of white light.
Initially distorted underwater images are preprocessed for restoration, where we are balancing the white content and enhancing the contrast.

## Slide 19: CLAHE
Enhancing the underwater images called mixture CONTRAST LIMITED ADAPTIVE HISTOGRAM EQUALIZATION (CLAHE) color model. The method operates Contrast Limited Adaptive Histogram Equalization on RGB and HSV color model and Euclidean norm is used to combine both results together. The combined results show less mean square error and high peak signal to noise ratio(PSNR) then other methods of under water image enhancing. It shows that the projected method is capable of classifying coral reefs particularly when visual cues are visible.

## Slide 20: ADVANTAGES
high accuracy
able to recover important faded features and edges

## Slide 21: SOFTWARE REQUIREMENTS:
MATLAB 2018(A)
MATLAB is a scientific programming language and provides strong mathematical and numerical support for the implementation of advanced algorithms. It is for this reason that MATLAB is widely used by the image processing and computer vision community. New algorithms are very likely to be implemented first in MATLAB, indeed they may only be available in MATLAB. We used Computer Vision and Image Processing Tools.

## Slide 22: REFERENCES
[1] Howell,E., 2014, ”Mars Curiosity: Facts and Information,” from http://www.space.com/ 17963 mars curiosity.html
[2] Marlos Dantas Baraga Brazil,2016 Symposium on augmented and virtual reality”technology integration of immersive virtual reality on smartphone with real-time motion capture”2016 IEEE DOI 10.1109/ SVR_2016
[3] Allen, P.K.; Timcenko, A.; Yoshimi, B.; Michelman, P., ”Automated tracking and grasping of a moving object with a robotic hand-eye system,” inRobotics and Automation, IEEE Transactions on, vol.9, no.2, pp.152- 165,Apr 1993.
[4] Marin, G.; Dominio, F.; Zanuttigh, P., ”Hand gesture recognition with leap motion and Kinect devices,” in Image Pro cessing (ICIP), 2014 IEEE Inter-national Conference on, vol., no., pp.1565-1569, 27-30 Oct. 2014.
[5] Ronald T. Azuma, A Survey of Augmented Reality, In Presence: Teleoperators and Virtual Environments 6, 4 (August 1997), 355-385